## Slide 1: Injection Safety
IPV Global Workshop
March 25, 2014

## Slide 2: Outline
Background
IPV
Injection Equipment
Waste Disposal

## Slide 3: Injection Use Worldwide
95% are for therapeutic purposes
5% are immunization injections
1% are used for injectable contraceptives
1% are of blood and blood products
> WHO estimates 50% of injections in developing countries are unsafe….
www/who/int/mediacentre/factsheets/fs231/en. Oct 2006

## Slide 4: Safe injection
No harm
“Immunization injections are only safe when the correct vaccine is properly administered with a sterile injection device that is disposed safely”
WHO recommended policy

## Slide 6: Unsafe practices
Pre-filling syringe with vaccine
Re-capping needle
Re-using needles and/or syringes
Improper waste disposal

## Slide 7: Factors that contribute to disease transmission
Overuse of therapeutic injections
Shortage injection equipment
Poor waste disposal practices
Re- use of syringes and needles

## Slide 8
Inactivated Polio Vaccine 1 dose

## Slide 9: Administration of IPV
Delivered intramuscular (IM)
Delivered subcutaneous (SC)
Requires syringe and needle
Mono dose
Multi dose

## Slide 10: Safe Injection Equipment
All countries should be using only auto-disable syringes or syringes with re-use prevention feature.
Auto-disable syringes and safety boxes should be supplied in adequate quantities for campaigns and routine immunization services

## Slide 11: Sterile Injection Device
A-D (auto-disable) needle and syringe--locks plunger after one use
Internal mechanism blocks plunger once it is fully pressed.
LOCK !
Injection stroke

## Slide 12: Sterile Injection Devices
GOOD: Disposable needle and syringe
  Without recapping needle
  Without re-using needle and syringe
  BEST: Syringes with re-use or needle stick prevention features
  Re-use by HCW’s or patients
  Needle related injuries and infections

## Slide 13: Needle Free Devices
Jet-Injectors
  Used for Smallpox Eradication
  Cross contamination concern
  Human and animal testing for new devices
Aerosol administration
  Measles vaccine—clinical trials in Mexico Influenza vaccine

## Slide 14: Hub Cutter
Syringe hub cutter
  Destroys needle and syringe to prevent reuse
  Reduces volume of waste

## Slide 16: Safe Disposal
“The collection, storage and subsequent destruction of all syringes and needles to avoid any accidents”

## Slide 17: Safety Boxes:
Sharps containers used for the disposal of safe and convenient disposal of syringes, needles and other sharps.

## Slide 18: Waste Disposal
Permanent
  Incineration
  Burning
    In a metal drum
    Open pit
  Burial
    Encapsulation

## Slide 19
Incinerator

## Slide 20
Metal Drum

## Slide 21
Open Shallow Pit

## Slide 22
Deep Open Pit

## Slide 23
Waste Disposal
Burial

## Slide 24: Resources
Guiding principles to ensure injection device security—WHO 2003
  http://www.who.int/injection_safety/WHOGuidPrinciplesInjEquipFinal.pdf
Aide memoire and checklist for injection safety—WHO 2003
  (http://www.who.int/vaccines-documents/DocsPDF04/www775.pdf)
Safe Injection Global Network (SIGN)
  http://www.who.int/injection_safety/sign/en/